## Slide 1
Quality Risk Management, ICH Q9(R1)
Training Slides
Risk Review
International Council for Harmonisation of Technical Requirements
for Pharmaceuticals for Human Use

## Slide 2: Legal Notice
This presentation is protected by copyright and may, with the exception of the ICH logo, be used, reproduced, incorporated into other works, adapted, modified, translated or distributed under a public license provided that ICH's copyright in the presentation is acknowledged at all times. In case of any adaption, modification or translation of the presentation, reasonable steps must be taken to clearly label, demarcate or otherwise identify that changes were made to or based on the original presentation. Any impression that the adaption, modification or translation of the original presentation is endorsed or sponsored by the ICH must be avoided.
The presentation is provided "as is" without warranty of any kind. In no event shall the ICH or the authors of the original presentation be liable for any claim, damages or other liability arising from the use of the presentation.
The above-mentioned permissions do not apply to content supplied by third parties. Therefore, for documents where the copyright vests in a third party, permission for reproduction must be obtained from this copyright holder.​

## Slide 3: Outline of this presentation
This presentation covers the following areas and topics pertaining to Risk Review:
Background and guidance
How Risk Review facilitates effective knowledge management
Risk Review's role in enabling continuous improvement
Planning a Risk Review
How existing elements of the quality system can facilitate Risk Review activities
What inputs might be considered as part of a Risk Review?
Considerations for Risk Review frequency
How Risk Reviews can support ICH Q12 implementation
The level of formality that may be applied to Risk Review activities
Risk Review Examples
Take-home points
Further Reading

## Slide 4: Risk Review – Background Information
In the original version of ICH Q9 (2005), Risk Review was addressed in Section 4.6.
While no changes were made to that Risk Review text during the guideline revision work, the topic of Risk Review was identified as one that required additional training materials.
In this regard the ICH Concept Paper for the ICH Q9(R1) revision work stated the following:.
“This work could provide additional clarity on the expectations relating to keeping risk assessments current and on the implementation of risk review activities based on lifecycle manufacturing performance and quality feedback. Risk review ties in with the concept of continuous improvement as expressed in ICH Q10 and in the lifecycle management guidelines (ICH Q12/Q14), and it could be addressed by developing additional training materials on this topic.”
The ICH Business Plan for ICH Q9(R1) stated the following about Risk Review:
“This targeted revision of ICH Q9 could also provide clarity in relation to risk review activities…” and “the revised guideline will provide additional guidance on… risk review.”

## Slide 5: What is Risk Review?
The purpose of risk review is to ensure that an ongoing state of control is maintained, and that knowledge, decisions and documentation are kept up to date:
Is the knowledge that the outputs from the QRM process were based on still valid and up to date?
Are all relevant hazards identified?
Are the risk control measures effective and adequate to control the risk?
Are the risk acceptance decisions still valid and up to date?
This can be achieved in a number of ways utilising a lifecycle approach and the existing elements of the Pharmaceutical Quality System.
“Review or monitoring of output/results of the risk management process considering (if appropriate) new knowledge and experience about the risk.”
Definition of Risk Review ICH Q9 R1

## Slide 6: ICH Q9(R1) provides the following guidance in relation to Risk Review
Risk Review
Risk management should be an ongoing part of the quality management process. A mechanism to review or monitor events should be implemented.
The output/results of the risk management process should be reviewed to take into account new knowledge and experience. Once a quality risk management process has been initiated, that process should continue to be utilized for events that might impact the original quality risk management decision, whether these events are planned (e.g., results of product review, inspections, audits, change control) or unplanned (e.g., root cause from failure investigations, recall). The frequency of any review should be based upon the level of risk. Risk review might include reconsideration of risk acceptance decisions (section 4.4).
Section 4.6 of the Guideline states the following:

## Slide 7: Risk and knowledge go hand-in-hand (1)
As knowledge increases, the ability to understand and control risk increases.
The cycle is continuous and perpetual; knowledge is always evolving and it should be continually applied to inform quality risk management activities.
Early in the product lifecycle, when less is known about a product and its manufacturing process, risk is higher.
Over time, knowledge increases due to items such as additional product and process development activities, manufacturing experience, and customer feedback, and this knowledge may be consolidated through activities such as, e.g., Risk Review.
This knowledge can (and should) be applied to reduce uncertainty, and therefore to reduce risk.
Level of understanding increases
Level of uncertainty decreases
Accuracy of risk estimation (and risk control) increases
Potential for patient harm decreases
Uncertainty
Knowledge
1. Lipa, M., O’Donnell, K., Greene, A: Knowledge as the Currency of Managing Risk: A Novel Framework to Unite Quality Risk Management and Knowledge Management, Journal of Validation Technology, Volume 26, Issue 5, October 2020

## Slide 8: Risk and knowledge go hand-in-hand
In a lifecycle approach using the Pharmaceutical Quality System, Risk Review can contribute signficantly to making sure that knowledge is actualised and kept up-to-date.
During development and technology transfer, it is important to establish knowledge about risk scenarios, so that those risks can be assessed and any required risk controls implemented.
In commercial manufacturing, day-to-day risk-based decisions are made to ensure the state of control is maintained.
Based on manufacturing and marketplace data, e.g. complaints, process performance is monitored, and new knowledge is used to update the risk scenarios and the control strategy (e.g. the original quality risk management documentation is reviewed and updated, where necessary).
Risk-reducing improvement initiatives are triggered.
The monitoring of performance data to capture new knowledge and trigger risk-reducing improvement initiatives is an important part of Risk Review.
Change Control, CAPA, and the reporting and escalation systems that may be in place for deviations and other issues are important inputs to Risk Review activities.

## Slide 9: Risk Review is important as it contributes to Risk-based Decision-making…
A Risk Review allows one to revisit a previous Risk Assessment exercise at some point in the future, to check whether its outputs and the decisions made during, and as a result of, that earlier risk assessment remain valid.
Such outputs and decisions may have related to what hazards existed at the time of an earlier risk assessment, the risks presented by those hazards, and how those risks should be managed.
With the passage of time, new knowledge and experience gained with the process or area that was risk assessed can help inform whether assumptions made during the decision-making process at that time remain valid now.
Such new knowledge and process experience may include new trend data (e.g. from PQRs, Control Charts, CpK reports, etc.) as well as data from deviations, out-of-specification batches, laboratory investigations, complaints, batch rejections, validation failures, etc.

## Slide 10: Risk Review & Continuous Improvement – in Risk Control
Risk review is also important with regard to risk control:
With the passage of time and the knowledge and experience gained about a process since an earlier risk assessment, Risk Review presents an opportunity to consider whether any risk controls that were implemented following the earlier Risk Assessment did actually deliver the level of risk reduction that was anticipated.
The performance and effectiveness of risk controls is important to check.
In this regard, Risk Review enables one to revisit (and potentially improve upon) the risk estimates that were previously assigned to hazards or failure modes on the basis of risk controls.

## Slide 11: Risk Review & Continuous Improvement - in Hazard Identification
Risk review is particularly important with regard to understanding what hazards exist:
It provides an opportunity to review the hazards that were considered during an earlier Risk Assessment exercise given the passage of time since then.
It allows one to determine how relevant those hazards still are, and whether any new hazards, not considered last time, should now be considered and risk assessed.
  If the earlier Risk Assessment exercise was performed on a new process, there may have been very little data to draw upon when identifying potential hazards and when assessing their risks.
  The passage of time may allow such data to be compiled and reviewed, so that better risk-based decisions can be made in relation to hazards and their related risks.
  For example, new hazards may come to light as a result of deviation issues, near miss incidents, and marketplace complaints.
  Such new knowledge about hazards represents improved process understanding.
  In this way, Risk Review contributes to ensuring the effectiveness of the Pharmaceutical Quality System (PQS) in line with ICH Q10, because it enables any risks associated with hazards to be managed more effectively, taking current knowledge about hazards into account.

## Slide 12: Managing Knowledge via Risk Review
Question:
Do you always need to plan risk review activities for a specific quality risk management process?
Answer:
No. Risk Review is used to react to new knowledge pertaining to quality risks and maintain the decisions and documentation of quality risk management activities to reflect current knowledge. This is relevant where the original quality risk management decision(s) may need to be changed based on new knowledge.
Some quality risk management processes can be considered single events, where the relevant knowledge is fed into, or results in, a revision of other risk assessments, where the knowledge is kept up to date for future use.
Change controls and deviation investigations are examples that can be such single event quality risk management processes, and these usually have a review element built into them (e.g., a change effectiveness check, or a CAPA effectiveness check), to ensure that the risks presented by the change or the deviation were adequately managed and, if new knowledge was captured, that it was fed into relevant systems where it should be maintained.
Such single events may not need a separate Risk Review.

## Slide 13: Planning Risk Review activities
It is useful to plan for Risk Review activities using a two-stage approach:
Stage 1: Plan for Risk Review as part of the outputs/results of the QRM process. Considerations here could include:
    Whether a Risk Review exercise needs to be performed on the process/item/area that was risk assessed.
    Whether any specific things should be reviewed during the Risk Review – e.g., the probability of occurrence of hazard X, or, the level of detection that a particular control has in relation to Risk Y, or, the degree of risk reduction that Control Z provided following its implementation.
    Whether any assumptions were made during the risk assessment – this is so that the validity of those assumptions can be checked during Risk Review.
    The areas where there were high levels of uncertainty or subjectivity during the risk assessment – this is so that these areas can be followed up on during Risk Review.
Stage 2: Review any new knowledge gained since an earlier Risk Assessment and use that knowledge when planning for Risk Review
    Such new knowledge may relate to increased process experience, increased process understanding, learnings made during change controls, deviations, complaint investigations, etc.
    This knowledge can be used to define areas that may need to be improved.

## Slide 14: Planning Risk Review cont’d
If it is decided that a Risk Review should be performed, it can be useful to consider the following:
The areas or parameters that should be reviewed during the Risk Review exercise
How those areas or parameters will be reviewed - i.e., what data will be needed, how will such data be analyzed, what analytical strategy should be used, etc.?
Whether there were any hazards identified during the earlier Risk Assessment that were not actually risk assessed during at that time and whether those hazards need to be revisited during the Risk Review exercise
Any issues, concerns or uncertainties that were present during the earlier risk assessment – this is so that they can be considered again during the Risk Review exercise
Any recommendations for the Risk Review team to consider that were made by the team that conducted the earlier Risk Assessment

## Slide 15: Is it useful for Risk Review to be performed on a periodic basis?
Setting up a risk review is done by considering a combination of two types of activities that go hand-in-hand:
Ongoing monitoring for new knowledge:
  Monitoring the effectiveness of Risk Controls (e.g., periodic metric reviews and parameter monitoring)
  Extracting any new knowledge that may be gained from planned events (e.g., change controls) and unplanned events (e.g., deviations, complaints)
Reviewing (and potentially revising) the documentation for the Risk Assessment and any decisions that arose from those
Activity 1 above can be used to trigger Activity 2, when new knowledge is identified
If Activity 1 provides a high degree of assurance that gaps in knowledge will be identified and addressed, and that any issues with Risk Control effectiveness will be resolved, then the need to repeat Activity 2 periodically is reduced or removed.
But if Activity 1 is more uncertain, the need for periodical review (Activity 2.) is higher.
Trigger
Activity 1. Ongoing monitoring for new knowledge
Effectiveness of Risk Controls
Planned events
Unplanned events
Activity 2. Reviewing (and potential revising) the QRM documentation and the related decisions
To ensure that these reflect current knowledge
The combination of Activities 1 and 2 helps ensure that QRM documentation and the related QRM decisions reflect reality and are periodically updated with current knowledge.

## Slide 16: Can existing elements of the Quality System contribute to Risk Review activities?
Yes, and within a pharmaceutical company, there are many elements of the Pharmaceutical Quality System (PQS) that can contribute to Risk Review activities
Product Quality Reviews (PQRs) / Annual Product Quality Reviews (APQRs) are an example.
  Typically conducted annually, these provide a means to review and assess process performance and the adequacy of the control strategy that is in place for a product.
  They also usually involve assessing Change Control and CAPA effectiveness.
  PQRs/APQRs are useful indicators of risk and residual risk levels, and they usually contain many different kinds of risk-indicating data and information:
    Batch QC data, in-process / process monitoring data, deviations, change controls, market complaints, rejections, reworks, Out-of-Specification (OOS) test results, stability data, validation data, etc.
  PQRs/APQRs can also be used to identify continual improvement opportunities that result in risk reduction – this is useful from a Risk Review perspective.
  PQRs/APQRs that are based on robust data collection and a strong analytical strategy (e.g., forecasting, predictive analytics, etc.), coupled with an appropriate review frequency, can facilitate the early identification of emerging risks and risk signals, including product availability risks.
But PQRs/APQRs do have some limitations:
By definition, they are retrospective in nature – such reviews are ‘after-the-fact’.
They may not have senior leadership visibility unless direct cost implications exist. If only lagging indicators are used to measure performance, the proactive identification of improvement opportunities to manage risks may be limited.

## Slide 17: Existing Quality System elements, cont’d
Management Review is another element of the Quality System that can contribute to Risk Review activities – this can apply to regulators as well as pharmaceutical companies
The review of data and performance measurements during Management Review can facilitate the identification of hazards that can affect the organization’s quality objectives
Management Review can proactively lead to continuous improvement initiatives that reduce risk and which have the clear support of Senior Management
It can assure the appropriate prioritization of changes and/or improvement initiatives based on risk assessment outcomes
Management Review can be used to promote ‘Plan Do Check Act’ activities that have Senior Management oversight and support
It can be used to evaluate process performance and the effectiveness of process changes and risk controls
It can facilitate Senior Management engagement in internal and external communications that relate to risk reduction
Management Reviews also have certain limitations, such as:
Such reviews are, by definition, retrospective in nature and they often have a fixed frequency - this can make them slow to react to fast emerging risk issues. (This can be addressed by ensuring that significant events can be escalated to Senior Management in a timely manner.)
If the right metrics / key performance indicators are not in place, the ability of Management Reviews to correctly identify process performance issues and the need for risk reduction can be limited.

## Slide 18: Existing Quality System elements, cont’d
ICH Q9(R1) states that the output/results of the risk management process should be reviewed to take into account new knowledge and experience, and that a mechanism to review or monitor events should be implemented.
It is important to recognise that there may be elements of the quality system that involve such review and monitoring activities, and these can serve as, or contribute to, Risk Reviews
They can feed knowledge back into, or require the revision of, the earlier assessment (e.g., a change control, or a deviation investigation).
Because they feed the knowledge into other assessments, they can be considered single events that do not require a separate risk review
Knowledge is kept up to date by ensuring risk review of the assessments that these single events feed knowledge into
Example – A deviation Incident
The deviation investigation after the incident identified the root causes of the issue and its contributory factors. This was new process knowledge.
This knowledge led to additional risk controls to prevent related incidents going forward.
The risk assessment that supported the deviation investigation was updated with the new knowledge and controls as a CAPA action
A separate Risk Review exercise was not planned for this particular deviation, as the knowledge gained was fed into the, now, updated related risk assessment.

## Slide 19: What to review during Risk Review…
Identifying ‘what to review’ is critical in executing effective Risk Review activities. The following can be useful items to review:
The outputs of a previous risk assessment and the decisions made – are they still valid?
Whether there are any new hazards that now need to be risk assessed on the basis of new knowledge gained since a previous risk assessment.
Whether all of the previously identified hazards are still relevant.
Whether all risks were assessed correctly – e.g., were all probability estimates supported?
Those aspects of the risk assessment that were associated with significant levels of uncertainty or subjectivity – what new data and knowledge may now be available which may help reduce uncertainty or subjectivity and improve the outputs of the risk assessment?
Any other knowledge gaps that were present during the earlier risk assessment - can these gaps now be addressed? What new knowledge has been gained about them since that risk assessment was performed?
The effectiveness of any risk controls that were implemented to reduce or control risk - did those risk controls deliver the expected level of risk reduction?
The current state of control – do any improvement opportunities exist that need to be considered?
Whether any new hazards were introduced as a result of the risk controls that were implemented following the earlier risk assessment.

## Slide 20: How frequently should Risk Reviews be performed?
The frequency or timing of a Risk Review exercise may be based on the type and number of risks identified during an earlier Risk Assessment exercise, and on the extent of risk control that was required to mitigate risks.
It may also depend on the level of uncertainty (i.e., lack of knowledge) that was present during an earlier risk assessment.
The higher the level of uncertainty in relation to risk estimates and the related risk-based decisions, the greater the need to review those estimates and decisions at an early timepoint, once such uncertainties have been reduced.
It is not possible to give definitive guidance here, because, as ICH Q9(R1) states, the frequency of Risk Review should be based on the level of risk.
?
?
?

## Slide 21: What to review, cont’d
Below are examples of indicators of performance and effectiveness that can be considered during a Risk Review exercise – this is not an exhaustive list:
CAPA effectiveness and timeliness
% of deviations that are considered repeat deviations
% of assigned root causes that are classified as human error
Change management effectiveness
Process capability/performance
  Statistical process control charts – process monitoring
  Cpk / Ppk indices
  Right-first-time; deviations, rejections, reworks
Production
  Overall equipment effectiveness – capacity and throughput
  Unplanned maintenance
  Yield and scrap
Supply chain oversight – establishing an effective monitoring strategy
  Delivery performance
  Customer feedback mechanisms – complaints
  Stock-outs and inventory
  Audits / inspection findings
  Effective quality agreements providing transparency and data sharing

## Slide 22: Risk Review frequency, cont’d
  The frequency of Risk Review activities may also depend on any recommendations made at the end of an earlier Risk Assessment exercise.
Example A
A Risk Assessment team that performed a risk assessment on a manufacturing process shortly after commercial manufacturing commenced, recommended that a particular risk be reviewed at an early time-point in the future, perhaps three months from the date of the Assessment, when more process data and experience would be available.
Because there was a high degree of uncertainty in its probability of occurrence rating, a decision was made that a) a Risk Review was required and b) it should be performed in three months’ time.
Example B
A Risk Assessment team found that the identification of hazards had been especially difficult, because the process being risk assessed was new to the site and quite novel in its use of advanced monitoring technologies.
There were also limited data and process experience to identify potential hazards.
Based on the high uncertainty of the knowledge available and the complexity of the setup, the Risk Assessment team decided that a Risk Review exercise should be performed 3 months’ after the original Risk Assessment, to consider if data and experience would confirm the initial assessment and conclusions, or if any new hazards might be identified or if control effectiveness might be inadequate.

## Slide 23: Risk Review & Product Lifecycle Considerations…
Risk Review can play an important role here. For example, Risk Review activities can lead to the following:
The proactive management of new and emerging hazards – this is because such hazards can be identified during Risk Review activities;
Maximizing the use of knowledge gained – this in turn can led to more objective/data-driven decisions, where uncertainty is reduced;
The identification of continual improvement opportunities;
Productivity optimization and efficiency gains;
Improved collaboration with supply chain partners;
Increased management commitment and employee engagement.
The implementation of ICH Q12 and its associated regulatory flexibilities is dependent upon the robust management of change and risk through an effective pharmaceutical quality system.

## Slide 24: The level of formality that may be applied during Risk Review
The following points are useful to consider:
ICH Q9(R1) provides guidance in relation to Formality in QRM – see Section 5.1 of the Guideline. That guidance is useful to consider when performing Risk Review activities.
When performing a Risk Review, it is important to consider:
  The level of importance of the risk assessment or other QRM activity that is being reviewed, from a patient safety and product quality perspective;
  The degree of uncertainty that existed when the earlier risk assessment or other QRM activity had been performed;
  The level of complexity that was associated with the risk assessment or other QRM activity that is being reviewed.
  A combined view of importance, uncertainty and complexity can help drive the level of effort and formality that is applied during Risk Review when evaluating the state of control
  The level of formality should also reflect the degree of knowledge that was available during the earlier risk assessment or other QRM activity. If knowledge was low on certain points, the Risk Review could be designed so as to seek and apply the missing knowledge.

## Slide 25: The next few slides provide examples illustrating the role of Risk Review

## Slide 26: Example 1: A Rogue Tablets issue (tablet mix-up)
A Risk Assessment exercise was performed on a primary packaging process (tablets in blister strips) at the end of the first year of commercial manufacturing
The potential for rogue tablets to be present on the packaging line was risk assessed – this involved an FMEA.
There had been two failed clearances of the packaging line (detected by QA) during the previous year.
The risk relating to rogue tablets was assessed, and risk control measures were required.
A risk control measure relating to a re-design of the hopper on the packaging line was proposed, to prevent tablets remaining in the hopper at the end of a packaging run.
The risk was re-assessed on the basis of this risk control, and the residual risk was considered to be low. The risk control was implemented.
With the passage of time, however, the data indicate that this risk control did not sufficiently reduce the risk associated with this issue – there had been two instances since that time when rogue tablets on the packaging line went undetected at the manufacturing site and which led to complaints from the marketplace.

## Slide 27: Example 1 cont’d
A Risk Review exercise was triggered following these complaints:
This involved a review of the FMEA and the performance of the risk control (hopper re-design).
The Risk Review also considered the fact that there had been another failed line clearance (again detected by QA) since the risk assessment had been performed.
The Risk Review concluded that the new risk control was not a reliable preventative measure for the rogue tablet incidents.
  It found that the root causes of most of the rogue tablet issues did not relate to the hopper at all. Other parts of the packaging line were found to be susceptible to the retention of tablets at various locations.
  Further significant packaging line changes were identified and implemented, reducing the potential for tablets to become trapped on the line.
  Since those line re-design changes, no line clearance failures had occurred, and no rogue tablet complaints had been received from the marketplace.
The Risk Review directly led to these equipment-related improvements, and a higher level of Risk Control was the result.
The Risk Review led to an update of the FMEA to reflect the new knowledge and the enhanced risk controls. This represented Continuous Improvement, as it resulted in improved assurance of product quality.

## Slide 28: Example 2: An Elemental Impurities Issue
Consider the risk of a drug (medicinal) product exceeding the elemental impurity limit in ICH Q3D for Lead.
Following the implementation of ICH Q3D, a manufacturer of the drug (medicinal) product performed a risk assessment to assess the presence of elemental impurities in the product,
It concluded, based on limited test results and excipient supplier Certificates of Analysis (COAs), that the risk of having unacceptable levels of lead in the product was high.
During this risk assessment, one excipient in particular was estimated to contribute more lead to the finished drug (medicinal) product than all the other excipients combined.
This was Magnesium Aluminium Silicate, a naturally occurring material that is mined from the earth and used by a range of industries, not just the pharmaceutical industry.
As a remediation action the manufacturer of the drug (medicinal) product ceased product release and it initiated testing of multiple batches of this excipient to update the initial risk assessment.
This testing revealed that the lead levels in the Magnesium Aluminium Silicate batches were much lower than those stated on the COAs from the supplier – it became evident that the COAs listed the maximum limit for lead as applied by the supplier, not the actual lead level in each batch.
This was an important learning which was fed back into the Risk Assessment.

## Slide 29: Example 2 cont’d
Furthermore, as a risk control measure, the company started testing all incoming Magnesium Aluminium Silicate batches for lead (it hadn’t been doing this until then).
This enabled the company to ensure that no high lead excipient batches would be used in production.
During Risk Review, these new test data as well as the new risk control that had been implemented were considered.
  The risk of exceeding the ICH Q3D limit for lead in the product was consequently reviewed - it was found to be lower than in the risk assessment, and the risk was found to be acceptable.
  This revised understanding of the risk was more accurate, as it was based on more robust data and on new information.

## Slide 30: Example 3: Continuous Improvement of a Contamination Control Strategy
During the risk-based establishment of the Contamination Control Strategy (CCS), the company had identified monitoring systems for each risk control measure
The effectiveness of the risk control measures is monitored on an ongoing basis for trends and events (i.e. monitoring for triggers)
The monitoring data, trend reports and conclusions are fed into other review systems, such as, e.g., ongoing process verification, Annual Product Quality Review and Management Review
If trends or deviations are found, this triggers an investigation in the CAPA system
Such investigations include a review of the current CCS to determine whether new knowledge has been obtained.
New knowledge might trigger an action to update the CCS documentation, or it may lead to changes in the CCS
Similarly, other changes may flag a need to update the CCS based on the knowledge gained from such changes
A periodic review of the CCS documentation is initially set yearly (as a minimum – this is to address the uncertainty that may be present in monitoring system effectiveness and because of the importance of contamination control).

## Slide 31: Take-home Points/Conclusions
Effective Risk Reviews can fill knowledge gaps and reduce uncertainty, leading to risk reduction:
  New knowledge can be gained through development, manufacturing experience, and customer feedback, and these, as well as other data sources, are useful to review.
It is useful to consider a two-stage planning process for Risk Reviews, and to leverage the insights of the initial risk assessment team.
Risk Reviews enable effectiveness assessments of risk controls and change controls (i.e., validating the effectiveness of risk controls and change controls).
An effective Risk Review framework is dependent upon:
  An appropriate frequency for conducting the Risk Review, that considers the levels of uncertainty, importance, and complexity. (See the ICH training material on Formality in QRM for guidance in relation to these three areas.)
  A robust data collection strategy that utilizes measures/indicators that are representative of performance and optimizes frequency of data collection.
Risk Review activities can be informed through existing elements of the Pharmaceutical Quality System (PQS).
Risk Reviews can help identify continual improvement opportunities which can lead to risk reductions, as well as efficiency gains.
Risk Reviews are foundational to effective change management and product lifecycle management. Thus, they support the implementation of ICH Q12.

## Slide 32: References
1. Lipa, M., O’Donnell, K., Greene, A: Knowledge as the Currency of Managing Risk: A Novel Framework to Unite Quality Risk Management and Knowledge Management, Journal of Validation Technology, Volume 26, Issue 5, October 2020

## Slide 33: Further Reading
ISO 31000 Risk Management Standard, § 5.4 & § 5.6
ISO 31010 Risk management — Risk assessment techniques, § 6.4.3
WHO guidelines on quality risk management (25.10.2017), § 3.6
PDA Technical Report No. 54: Implementation of Quality Risk Management for Pharmaceutical and Biotechnology Manufacturing Operations (2012 –2019), § 4.5
PDA Technical Report No. 68: Risk-Based Approach for Prevention and Management of Drug Shortages (2014), § 6
ISPE Baseline Guide Vol 7: Risk-Based Manufacture of Pharmaceutical Products (2017), § 12
NASA S3001: Guidelines for Risk Management, October 16, 2017, Page 13, § Risk Review

## Slide 34: EWG Acknowledgment and Contact
Acknowledgement to ICH Q9(R1) Expert Working Group (EWG)
For any questions, please contact the ICH Secretariat:
admin@ich.org