## Slide 1
Quality Risk Management, ICH Q9(R1)
Training Slides
Hazard Identification – Part II
Considerations in Relation to Identification of Failure Modes in the Pharmaceutical Environment
International Council for Harmonisation of Technical Requirements
for Pharmaceuticals for Human Use

## Slide 2: Legal Notice
This presentation is protected by copyright and may, with the exception of the ICH logo, be used, reproduced, incorporated into other works, adapted, modified, translated or distributed under a public license provided that ICH's copyright in the presentation is acknowledged at all times. In case of any adaption, modification or translation of the presentation, reasonable steps must be taken to clearly label, demarcate or otherwise identify that changes were made to or based on the original presentation. Any impression that the adaption, modification or translation of the original presentation is endorsed or sponsored by the ICH must be avoided.
The presentation is provided "as is" without warranty of any kind. In no event shall the ICH or the authors of the original presentation be liable for any claim, damages or other liability arising from the use of the presentation.
The above-mentioned permissions do not apply to content supplied by third parties. Therefore, for documents where the copyright vests in a third party, permission for reproduction must be obtained from this copyright holder.​

## Slide 3: Agenda
What are the benefits of separate training material in relation to failure modes?
Concepts and terminology
Process flows for failure modes, hazards, hazardous situations and their impact on patients
Linking Preliminary Hazard Analysis (PHA) with Failure Mode Effect Analysis (FMEA)
Strategies for better failure mode identification
How human error can be an indicator that a proactive approach to Quality Risk Management (QRM) is needed

## Slide 4: What Are the Benefits of Separate Training Material on Failure Modes ?
What are the benefits of this training material?
Reduce confusion between concepts/terms related to QRM and its tools
Provide tips and techniques on how to better identify and document failure modes
Illustrate how the QRM tools may link hazards to failure modes
Explain how investigating human error issues is beneficial to help identify underlying failure modes or hazards to product quality
See ICH Q9(R1) and the training material on Hazard Identification for more details
ICH Q9(R1) refers to “Hazard Identification” as the first step of the QRM process.
“Hazard” is a concept from ICH Q9(R1) while “Failure Mode” is a tool-specific term used in risk assessment tools such as, FMEA and Failure Mode Effect & Criticality Analysis (FMECA). Such tools do not usually refer to “Hazards”.
These tools are very widely used in the pharmaceutical environment, and therefore it is necessary to explain in this training material how “Hazard” and “Failure modes” are inter-connected.

## Slide 5: Key Terms & Concepts
There can sometimes be confusion between concepts/terms related to QRM and its tools, and because certain terms are tool-specific, they need to be used in the appropriate context
Potential source of harm
(to patient health, product quality or product availability)
Damage to health, including damage from a loss of product quality or availability
Probability of occurrence of harm and severity of harm
(R = P x S)
ICH Q9(R1) Concepts
Hazard
Harm
Risk
PHA terminology: event or circumstance causing exposure to the hazard
FMEA terminology: the ways or modes in which a product, process or system might fail
Tool-specific Terminologies
FTA terminology: the ways or modes in which a product, process or system might fail
Hazardous Situation
Failure Mode
Fault
‘Hazard’ is a concept from ICH Q9(R1), while “Failure Mode” is a tool-specific term often used during QRM activities.
The QRM process in ICH Q9(R1) refers to Hazard Identification as the first step of the Risk Assessment process.
Hazards and failure modes are different from each other:
  A hazard is a potential source of harm to the patient.
  A failure mode is the specific way a failure occurs.
  Like hazards, failure modes can lead to patient harm if the associated failures occur that impact product quality.
While some risk assessment tools refer to hazards (e.g., HACCP - Hazard Analysis and Critical Control Points, HAZOP - Hazard Operability Analysis, PHA - Preliminary Hazard Assessment), others do not – other tools refer to failure modes (e.g., FMEA - Failure Mode and Effect Analysis, FMECA - Failure Mode, Effects and Criticality Analysis), while some other tools refer to faults (e.g., FTA - Fault tree analysis).
In this way, the ICH Q9(R1) concept of a “hazard” and the tool-specific term “failure mode” are inter-connected.

## Slide 6: Failure Mode ID QRM Tools: FMEA
To ensure that risks are captured, particularly by tools such as FMEA, the risk question (what could go wrong?) is asked at each process step and the response is documented and the FMEA may be used in conjunction with other Hazard ID tools (e.g., preliminary hazard analysis, Ishikawa fishbone, process mapping, etc.)
FMEA identifies known and potential failure modes of processes, facilities, systems, products, equipment, or components by specifically asking "What could go wrong?”
The impact of each failure is the potential source of patient harm (i.e., hazard).
An ineffective equipment cleaning procedure (failure mode) can cause cross contamination issues (potential failure effect) that may cause a drug product to contain an unwanted drug (potential failure impact)
Incorrect stopper placement on the vial during primary packaging (failure mode) can cause container closure integrity issues (potential failure effect) that may lead to biological contamination of a product
(potential failure impact)
"What could go wrong to cause a drug product to become contaminated?”
Failure Mode Effects Analysis (FMEA) is one of the frequently used tools to identify the way a product/process/system might fail and the likely effects on product quality that can lead to patient harm
QRM TIP:
See the ICH Q9(R1) training materials on Formality in QRM and Subjectivity in QRM to determine the right tools for the risk assessment.

## Slide 7: Failure Mode – Example 1
Failure Mode
The manner in which a sterile filling line is exposed to biological contamination
Hazard
Biologically contaminated medicine is the potential source of harm that can impact patient health
Hazardous Situation
Injection of medicine with biological contamination which may lead to patient harm
Harm
Illness (potentially severe) or even death​ of the patient
Damage to health caused by patient exposure to medicine with biological contamination
Impact of the Failure
Biological Contamination of Medicine
Operator intervention ​
Equipment​ design flaw
Deficient cleaning
Inappropriate packaging
Risk
The combination of probability of occurrence of patient harm by injection of medicine with biological contamination (Hazardous Situation)
and the severity of that Harm
Multiple Failure Modes can lead to the same hazardous situation
Failure Modes lead to Hazardous Situations and may ultimately lead to patient harm

## Slide 8
Hazard
Biologically contaminated API (i.e., hazard).
Harm
Illness (potentially severe) or even death​ of the patient
Damage to health caused by patient exposure to medicine with biological contamination
Inadequate equipment sterilization
Risk
The combination of probability of occurrence of patient harm by lack of availability of a critical medicine (Hazardous Situation)
and the severity of that Harm (untreated illness)
Failure Mode – Example 2
Failure Mode
Inadequate equipment sterilization
Impact of the Failure
Biological Contamination of Active Pharmaceutical Ingredient (API)
Hazardous Situation
Injection of medicine with biological contamination.
The Hazardous Situation and Harm were prevented via the risk controls that were in place.

## Slide 9
Hazardous Situation
Lack of product availability of the critical drug product may lead to patient harm
Harm
Untreated illness (potentially severe) or even death​ of the patient due to lack of availability of a critical drug product
Hazard
Lack of supplier reliability for a critical drug product component (i.e., API) and hence lack of product availability of a critical drug product that can lead to patient harm
Failure to maintain a state of control for microbial contamination
Risk
The combination of probability of occurrence of patient harm by lack of availability of a critical medicine (Hazardous Situation)
and the severity of that Harm (untreated illness)
The impact to product quality (e.g., biologically contaminated API ) of an initial failure can become a root cause of another failure (e.g., loss of a state of control). The effect of the new failure leads to cessation of manufacturing that may impact supply reliability for a critical drug product API (i.e., hazard) and hence lack of product availability that may ultimately lead to patient harm.
Failure Mode – Example 3
Failure Mode
Failure to maintain a state of control for microbial contamination
Impact of the Failure
Lack of supplier reliability

## Slide 10: Failure Mode Strategies
1. Prepare for Better Brainstorming
2. Evaluate the Number of Causes Associated with each proposed Failure Mode when evaluating the proposed Failure Mode
3. Encourage and Capture the Reporting of Near Miss Incidents
4. Do not Merely Map the Process, assemble Comprehensive Data on the item under study
5. Look for Strength of Evidence when Expert Judgment and Informed Opinions Are Used
There are certain strategies (1) that can be used for better identifying and documenting failure modes, and each is explored in the following slides.
  O’Donnell, K., Greene, A., Failure Modes - Simple Strategies for improving qualitative Quality Risk Management exercises during Qualification, Validation and Change Control Activities, Journal of Validation Technology, Vol. 13, No. 2, 2007

## Slide 11: 1. Better Brainstorming
Brainstorming is a useful way to identify potential hazards and failure modes, but it should be conducted in a structured way.
Prepare for better brainstorming by:
Ensuring that there are documented procedures in place for brainstorming;
Having the right people involved. For example, the QRM team can consist of technical experts who process-map, operators who identify failure modes, and clinical experts who determine harm to patient;
Ensuring that failure modes are documented at a level within the process being risk assessed so that meaningful root causes can be identified for them. This leads to more appropriate risk mitigation and control measures.
QRM TIP:
Confusion between failure modes, their causes and effects can occur in FMEA-based applica­tions. For example, the root cause of a particular failure mode could be considered a failure mode itself at a lower indenture level in the process or system that is being risk assessed. It is useful, therefore, to have the process clearly documented prior to conducting the FMEA, and to consider what level within the process is the most optimum to identify potential failure modes.

## Slide 12: 1. Better Brainstorming (cont’d.)
Ensuring that the failure mode is not the same as the failure mode effects or its root causes. The failure mode and root causes need to be well understood and documented.
Ensuring that any pertinent assumptions made relating to qualification and validation, which may be important for the controls related to specific failure modes, are discussed and are clearly documented.
Ensuring that any significant uncertainties in relation to failure modes are docu­mented.
QRM TIP:
Documenting uncer­tainties in the risk associated with the failure mode, or even accepting that the risk cannot be estimated at that time without additional data, can be useful.
QRM TIP:
Answer these questions "What can go wrong? What are the effects or consequences of this? at each step of the process. If the failure mode is the same as its effects, then it is not written correctly - work to redefine the failure mode for the identified effects.

## Slide 13: 2. Failure Modes at the right level...
  When considering proposed failure modes, it is useful to consider their potential causes before the failure modes are forward-processed through the risk assessment exercise. The reasons for this are as follows:
If a proposed failure mode has a very large number of potential causes, (i,e., it is very broad in scope), it can become practically unmanageable dur­ing the risk assessment exercise.
Examples of such failure modes would include: "Out-of-Specification Batches", "Loss of Sterility Assurance", "Product Contamination", etc.
Such failure modes have so many potential causes that they can be very difficult to adequately risk assess.
QRM TIP:
If more than 5 potential causes can be identified for a proposed failure mode, the failure mode is too broad, and it is probably written at too high an indenture level in the process or item being risk assessed. It should be broken down in several more specific failure modes that have fewer potential causes, and which will be more manageable.
QRM TIP:
Review each proposed failure mode and its causes to check whether the failure mode is documented at a workable level in the risk assessment.

## Slide 14: 3. Capturing Near Miss Incidents
When brainstorming for potential failure modes, it is of course important to review the obvious sources of information (such as data on process deviations, batch rejects, quality defects and other complaints, production problems, qualification and validation incidents/failures, reasons for change controls, etc.).
However, an area that is often overlooked is the occurrence of near miss events (i.e. incidents that almost occurred, but either didn’t, or their effects were not realized).
  Near miss incidents can provide valuable and real-life information on potential failure modes.
  Near misses can be treated as potential failure modes that can be included in risk assessments.
QRM TIP:
Consider encouraging a culture of reporting near misses within your organization, similar perhaps to how deviations are expected to be reported.

## Slide 15: 4. Compiling comprehensive data on the process or item under study
  It is usually not sufficient to just map the process or item under study to determine at which step failure modes may occur - process maps are often high level and provide limited information.
  It is useful if the QRM process defines the data and documentation required for failure mode identification, such as:
  The steps in the process or item under study in which human interventions occur;
  The master batch manufacturing record and SOPs for the process being risk assessed, including SOPs for any ancillary processes (e.g., for controlling room environment, taking samples, etc.);
  A list of the equipment used in the process;
  For change controls, the current and proposed process/procedure in sufficient detail to facilitate failure mode identification;
  Critical process controls as well as a list of in-process and finish product tests, with their specifications/limits;
  An outline of how the process works, and a description of any special technology that is used in the process – this is important for those risk assessment team members who may not be subject matter experts in the process being risk assessed or its technology.

## Slide 16: 5. Looking for Strength of Evidence
ICH Q9(R1) states in section 5.3 that: “Subjectivity can impact every stage of a quality risk management process, especially the identification of hazards...”
Involving experts in a QRM exercise is beneficial – it allows one to obtain informed opinions and expert judgements
But it is still important to consider the strength of evidence supporting such opinions and judgements – this is because biases and human heuristics can affect the opinions and judgements of experts
Looking for the strength of evidence can help reduce the level of subjectivity and guesswork that may be present
Other practical considerations include:
  Seek the opinions of actual users and operators of the process or item under study
  Seek the opinions of those employees or others who are knowledgeable in the process or item under study (e.g., the vendor of a specific equipment, who should know about known problems)
  Take into consideration views or concerns from stakeholders involved with the product.
    Example: If a change control is proposed to roll out a new la­belling and livery design for a range of medicinal products, practicing pharmacists may usefully ad­vise about risks of dispensing or usage errors which may be introduced by the change.

## Slide 17: Case Study: Linking Hazards to Failure Modes Step 1: Identifying Hazards
Critical Quality Attribute | Hazard | Sequence of Events | Hazardous Situation | Harm | Severity
Sterility | Biological contamination of the product | Drug product is contaminated during manufacture and user injects into blood stream | Exposure to bacteria or fungi | Severe illness or death | Catastrophic
Potency | Not enough active ingredient filled | Insufficient amount of active ingredient is added and user injects | Underdose | Flare of symptoms | Moderate
Hazard Analysis
One way of identifying hazards to drug product quality is to consider its Critical Quality Attributes (CQAs).
Note: The severity of harm may depend on the patient population, the disease indication and other factors.

## Slide 18: Case Study: Linking Hazards to Failure Modes Step 2: Linking Failure Modes with Hazards
A process FMEA can identify failure modes with potential product impact. What is the severity of these failure modes?
It is the severity assigned to the hazard they are leading to. This way, the hazard analysis from Step 1 can provide consistent guidance on risk ratings for failure modes.
FMEA relating to manufacturing
The black arrows on the left show how the potential product impact of a failure mode (QRM tool: FMEA) corresponds to a hazard in the other tool (QRM tool: Hazard Analysis). Consequently, the severity of harm associated with that hazard applies to all the failure modes in the FMEA that lead to that hazard. The severity corresponds to all FMEA line items associated with that hazard.
Requirement | Failure Mode | Potential Failure Effect | Potential Product impact | Severity | Potential Cause | Prevention Control | Detection Control | Occurrence | Detection | Risk
Correct stopper position in filled syringe | Stopper not positioned correctly | Container closure integrity impaired | Biological contamination of the product | Catastrophic | Servo motor lost position | 100% automatic equipment homing | Automatic visual inspection | Remote | High | Low
Critical Quality Attribute | Hazard | Sequence of Events | Hazardous Situation | Harm | Severity
Sterility | Biological contamination of the product | Drug product is contaminated during manufacture and user injects into blood stream | Exposure to bacteria or fungi | Severe illness or death | Catastrophic
Hazard Analysis

## Slide 19: Case Study: Linking Hazards to Failure Modes Step 3: Aligning Risk Ratings Across Multiple FMEAs
Several FMEAs for a product may include failure modes that lead to the same product impact (here: biological contamination of the product). In this example, the separate hazard analysis allows for consistent risk ratings across multiple FMEAs and aligned risk prioritization across the drug product.
FMEA relating to manufacturing
Requirement | Failure Mode | Potential Failure Effect | Potential Product impact | Severity | Potential Cause | Prevention Control | Detection Control | Occurrence | Detection | Risk
Correct stopper position in filled syringe | Stopper not positioned correctly | Container closure integrity impaired | Biological contamination of the product | Catastrophic | Servo motor lost position | 100% automatic equipment homing | Automatic visual inspection | Remote | High | Low
Critical Quality Attribute | Hazard | Sequence of Events | Hazardous Situation | Harm | Severity
Sterility | Biological contamination of the product | Drug product is contaminated during manufacture and user injects into blood stream | Exposure to bacteria or fungi | Severe illness or death | Catastrophic
Hazard Analysis
Correct stopper position in filled syringe | Stopper movement | Container closure integrity impaired | Biological contamination of the product | Catastrophic | Shaking and vibration during air transport | Protective shipping containers | Automatic visual inspection at receipt | Remote | High | Low
FMEA relating to distribution
Notes:   General Thoughts?
  (please add your name before feedback)
  Comments (including suggested revisions)

## Slide 20
The final part of this presentation focusses on Human Error
Investigating human error issues is beneficial, as it can help identify underlying Failure Modes or Hazards and the examples demonstrate an effective QRM approach

## Slide 21
Consider the following reference to human error in Chapter 8 - Complaints and Product Recall - of the PIC/S GMP Guideline (2)
(Section on Root Cause Analysis & CAPAs)
“An appropriate level of root cause analysis should be applied during the investigation of deviations, suspected product defects and other problems. This can be determined using Quality Risk Management principles.
In cases where the true root cause(s) of the issue cannot be determined, consideration should be given to identifying the most likely root cause(s) and to addressing those.
Where human error is suspected or identified as the cause, this should be justified, having taken care to ensure that process, procedural or system-based errors or problems have not been overlooked, if present.
Appropriate corrective actions and/or preventive actions (CAPAs) should be identified and taken in response to investigations. The effectiveness of such actions should be monitored and assessed, in line with Quality Risk Management principles.”
2. PIC/S GMP Guideline, PE 009-16 (Part I), Chapter 8 – Complaints and recalls, 2022
Human Error
Regulatory expectations

## Slide 22
What does human error indicate?
May be an indicator of poorly designed equipment (e.g., human/machine interface)
May be a symptom and not a cause for something to go wrong
May be an indicator of incomplete knowledge regarding the root causes of process variability (i.e., failure modes
May be an indicator of potential patient harm
Assigning human error as the root cause of an issue may sometimes be too simplistic. Rather, human error can trigger further analysis of the underlying process for failure modes.
QRM Tip
The words 'human error' may trigger the start of a QRM process, and is rarely the endpoint of an investigation
Human Error
An indicator that a proactive approach to QRM is needed

## Slide 23
What can be done to avoid incorrectly assigning human error as the root cause?
Understanding variability (e.g., in operator technique) may provide knowledge that is instrumental in correctly diagnosing the root cause(s) of human error, and implementing effective CAPAs, such as increasing automation, etc.
Risk Review presents an opportunity to further investigate and identify CAPAs to improve process robustness, ensuring the quality of the drug product to the patient.
Applying increased formality in QRM activities when investigating root causes may lead to the identification of the underlying factors (failure modes) that led to the human error.
QRM Tip
"A proactive approach to quality risk management is beneficial … and it is of strategic importance in achieving an effective Pharmaceutical Quality System. (See ICH Q10 for guidance)”
ICH Q9(R1)
Human Error
An indicator that a proactive approach to QRM is needed (cont.)
“An effective approach to QRM includes appropriate application of root cause analysis to identify and address root cause(s) and other causal factors, including human related ones.”
ICH Q9(R1)

## Slide 24
Human Error
How can human error be proactively managed to assure quality of products to patients?
Consider 3 examples from the pharmaceutical environment
Example 1
Sources of human variability may impact the quality of drug products, leading to potential patient harm. One way to gain knowledge on potential sources of human variability is by considering the operator experience.
Example 2
Human error can be an important indicator of poor process robustness. Risk Review activities present an opportunity to further investigate and identify CAPAs to improve process robustness to ensure the quality of drug products to the patient.
Example 3
Building robustness into facility and equipment design can prevent human (operator) error and ensure the quality of drug products to the patient.

## Slide 25: Human Error Example 1
One way of identifying human (operator) variability that may impact product quality is to analyze processes where critical Human-Machine Interactions are present.
The following is a list of possible areas where human factors for non-automated processes may be further examined to identify sources of variability (i.e., failure modes) that may potentially cause harm to the patient.
  Manual setup of equipment
  Fixing an equipment malfunction
  Routine equipment interactions (e.g., opening/closing valves)
  Performing manual cleaning steps and disinfection of processing line and room
  Routine interventions and non-routine interventions in aseptic manufacturing (e.g., fixing a vial jam). Examples:
    Charging containers or closures onto an aseptic filling line
    Clearance of units on the aseptic processing line due to major/extended intervention
  Manual transfers from one unit operation to another (charging and discharging)
  Preparing a sample for analysis (laboratory)
  Manual activities near an insufficiently protected aseptically filled product
  Maintained equipment that often requires repeated or extensive manual interventions
QRM TIP: An audit is a great way to gain knowledge on potential sources of human (operator) variability by considering the operator experience.

## Slide 26
Indicators of process performance and control effectiveness are often reviewed during Risk Review activities – e.g., % of assigned root causes that are classified as human error
When a Risk Review activity identifies a high rate of human error, this can relate to low capability facilities and equipment. Here, manufacturing performance can be significantly impacted by vulnerabilities to poorly designed human/machine interfaces, leading to process variability.
A high number of deviation cases in which human error is assigned as the root cause can be an indicator of a lack of knowledge about potential sources of human (operator) variability (i.e., failure modes) relating to poor process robustness that can impact product quality. This uncertainty can potentially lead to patient harm.
  One industry study found that approximately “50% of deviations are attributable to human error…Despite our best efforts the human error rate has been constant over several years.” This can indicate that increased formality is needed in QRM activities, in order to diagnose the underlying root causes of human error and process robustness issues, so that more effective CAPAs can be identified.
  Human error is often a symptom (or consequence) of an underlying problem, not the actual cause of the failure.
  Solutions to such problems can be in response to the knowledge gained about human error throughout the lifecycle
Human Error
Example 2

## Slide 27
Building robustness into facility and equipment design can help prevent human (operator) error and ensure the quality of drug products to the patient (3) (4)
Process capability and robustness can be increased by proactive process designs that make use of modern technologies, such as digitalization, automation, isolation technology, amongst others. This enhances both quality and efficiency.
For example, by improving quality, one can also increase efficiency, as follows:
Automation reduces/minimizes failure caused by manual variability, and it can lead to risk reduction.
Integration of automation across unit operations minimizes risks from failures related to manual transfers between unit operations.
Advanced testing and data analytics can increase process capability and lead to risk reduction when such technologies are fit for their intended use.
e.g., they can automatically adjust the process when aberrant conditions are detected via online monitoring/testing,
e.g., they can help diagnose root causes
Reducing risks to process robustness caused by human (operator) error can decrease costly failures and scrap. It can also enhance both quality and speed of production.
Human Error
Example 3
  3. Berry, C., et al. What Does It Really Look Like to Properly Address a “Human Error Problem” in Biopharma? The Human Performance Blue-Sky Description That Will Help Improve Industry Performance, PDA J Pharm Sci and Tech, 2019, 73(4)
  4. Wilson, A, et al. Changing the Performance Paradigm in Pharma/Biotech: Integrating Human Performance in Global Organizations, PDA J Pharm Sci and Tech, 2015, 69(5)

## Slide 28: References
  O’Donnell, K., Greene, A., Failure Modes - Simple Strategies for improving qualitative Quality Risk Management exercises during Qualification, Validation and Change Control Activities, Journal of Validation Technology, Vol. 13, No. 2, 2007
  PIC/S GMP Guideline, PE 009-16 (Part I), Chapter 8 – Complaints and recalls, 2022
  Berry, C., et al. What Does It Really Look Like to Properly Address a “Human Error Problem” in Biopharma? The Human Performance Blue-Sky Description That Will Help Improve Industry Performance, PDA J Pharm Sci and Tech, 2019, 73(4)
  Wilson, A, et al. Changing the Performance Paradigm in Pharma/Biotech: Integrating Human Performance in Global Organizations, PDA J Pharm Sci and Tech, 2015, 69(5)

## Slide 29: EWG Acknowledgment and Contact
Acknowledgement to ICH Q9(R1) EWG
For any questions please contact the ICH Secretariat:
admin@ich.org