## Slide 1
Quality Risk Management, ICH Q9(R1)
Training Slides
Hazard Identification – Part I
International Council for Harmonisation of Technical Requirements
for Pharmaceuticals for Human Use

## Slide 2: Legal Notice
This presentation is protected by copyright and may, with the exception of the ICH logo, be used, reproduced, incorporated into other works, adapted, modified, translated or distributed under a public license provided that ICH's copyright in the presentation is acknowledged at all times. In case of any adaption, modification or translation of the presentation, reasonable steps must be taken to clearly label, demarcate or otherwise identify that changes were made to or based on the original presentation. Any impression that the adaption, modification or translation of the original presentation is endorsed or sponsored by the ICH must be avoided.
The presentation is provided "as is" without warranty of any kind. In no event shall the ICH or the authors of the original presentation be liable for any claim, damages or other liability arising from the use of the presentation.
The above-mentioned permissions do not apply to content supplied by third parties. Therefore, for documents where the copyright vests in a third party, permission for reproduction must be obtained from this copyright holder.​

## Slide 3: Agenda
This training material is designed to help one learn about:
The 2023 revision to ICH Q9 which replaced “Risk Identification” with “Hazard Identification”.
How hazards and risks differ from each other.
How hazards may be identified and documented, and why doing this step first during the risk assessment process is essential to ensure effective Quality Risk Management process.
How hazards, hazardous situations and failure modes are linked.
A case study illustrating decision making in relation to which hazards to be assessed via risk assessment activities
There are also key take-home points.
​
* Note: Specific information in relation to the identification of Failure Modes is given in Part II of this presentation - ‘Considerations in relation to Failure Modes in the Pharmaceutical Environment’

## Slide 4: Background to the Hazard ID Revision
  Question:
  The original version of ICH Q9 already referred to the identification of hazards in Section 4.3, ‘Risk Assessment’. Why then was the terminology revised in ICH Q9(R1) (1), from ‘Risk Identification’ to ‘Hazard Identification’?
  Answer:
This terminology change aligns with the definition of risk assessment in ICH Q9. It also aligns with the expectation to identify hazards to product quality* that may potentially lead to patient harm; moreover, it may improve how hazards are perceived and assessed.
Risk Assessment section (4.3) in the guideline correctly referred to the identification of hazards. However, another part of that same section, which also referred to the identification of hazards, was incorrectly titled Risk Identification. In addition, the Figure 1 schematic of the QRM process in the same section of the guideline referred to Risk Identification and not Hazard Identification. This was incorrect, and therefore the terminology was changed to refer only to the identification of hazards, not to the identification of risks. (2)
* Note: In line with ICH Q9(R1), the references in this training material to impact to product quality are understood to also include impact to product availability.

## Slide 5: The Hazard ID Revision
Figure 1 (1) in the Guideline was changed as shown below – from 'Risk Identification' to ‘Hazard Identification'
The revision illustrates that 'Hazard Identification' is the first step in the Risk Assessment
OLD
NEW

## Slide 6: Hazards and Risks Are Not the Same
Hazard
Potential source of harm
(to patient health, product quality or product availability)
Harm
Damage to health, including damage from a loss of product quality or availability
Risk
probability of occurrence of harm and severity of harm
(R = P x S)
Understanding the differences above can lead to improvements in “...how risks are assessed and how hazards, risk, and harms are perceived by different stakeholders”. (1)
… before a risk can be assessed
These need to be clear…
  During hazard identification, risk is not yet a consideration.
  The focus is on hazards. And for each hazard, it is useful to consider the harm that it may lead to.
  Harm can relate to patients, as well as the impact on product quality or availability.

## Slide 7: What are the benefits of this change in terminology?
Highlights the need to identify hazards and not risks during the first step of the risk assessment process, to remove any distractions about risks that may interfere with the hazard identification activity.
Example: When a Risk Assessment team is focused only on identifying hazards, they do not have to think about any related probabilities of occurrence - they only have to consider what the potential hazards may be in relation to the risk question under consideration.
This is also the case in relation to severity of harm – during hazard identification, there is no need to spend time working to estimate the severity of the harm that may be presented by a hazard; that comes later, after the hazards have been identified.
The change from “Risk Identification” to “Hazard Identification” can bring several benefits
7
Ultimately, this small change in terminology has the potential to lead to better risk-based decisions and more effective QRM outputs generally.

## Slide 8: What are the benefits of this change in terminology? (cont’d)
8
perhaps it lacks procedural control?
Focus on hazard identification may lead to more attention being paid to exactly how hazards get identified – and if improvements in this area are needed, these can be made.
Example, if a pharmaceutical company or a regulatory authority examines how hazards are identified in their QRM process, they may realise that the hazard identification step is poorly developed within their organisation
perhaps there is little opportunity for creative thinking?
perhaps it makes little use of structured tools that can aid with hazard identification?
QRM TIP:
Creative thinking during hazard identification is important – see slide 18 for information.

## Slide 9: Key Terms & Concepts
There can sometimes be confusion between concepts/terms related to QRM and its tools, and because certain terms are tool-specific, they need to be used in the appropriate context
Potential source of harm
(to patient health, product quality or product availability)
Damage to health, including damage from a loss of product quality or availability
Probability of occurrence of harm and severity of harm
(R = P x S)
ICH Q9(R1) Concepts
Hazard
Harm
Risk
PHA terminology: event or circumstance causing exposure to the hazard
FMEA terminology: the ways or modes in which a product, process or system might fail
Tool-specific Terminologies
FTA terminology: the ways or modes in which a product, process or system might fail
Hazardous Situation
Failure Mode
Fault
‘Hazard’ is a concept from ICH Q9(R1), while “Failure Mode” is a tool-specific term often used during QRM activities.
The QRM process in ICH Q9(R1) refers to Hazard Identification as the first step of the Risk Assessment process.
Hazards and failure modes are different from each other:
  A hazard is a potential source of harm to the patient.
  A failure mode is the specific way a failure occurs.
  Like hazards, failure modes can lead to patient harm if the associated failures occur that impact product quality.
While some risk assessment tools refer to hazards (e.g., HACCP - Hazard Analysis and Critical Control Points, HAZOP - Hazard Operability Analysis, PHA - Preliminary Hazard Assessment), others do not – other tools refer to failure modes (e.g., FMEA - Failure Mode and Effect Analysis, FMECA - Failure Mode, Effects and Criticality Analysis), while some other tools refer to faults (e.g., FTA - Fault tree analysis).
In this way, the ICH Q9(R1) concept of a “hazard” and the tool-specific term “failure mode” are inter-connected.

## Slide 10
Hazards and Risks are not the same...
Consider this real-world Risk Scenario
Hazardous Situation
An exposure to a Hazard (the bomb)
Risk
Is the combination of probability of occurrence of harm through exposure to the hazard (the bomb) and the severity of that harm (being injured by the explosion).
Hazard
Potential source of harm (the bomb)
Harm
Damage to health caused by exposure to hazard
(the bomb)
The Hazard leads to the Hazardous Situation
The Hazardous Situation may lead to Harm

## Slide 11: Hazards and Risks are not the same... Consider this Pharmaceutical Risk Scenario
Hazard:
Biological contamination of the drug product is the potential source of harm (hazard) that can impact patient health
Hazardous Situation:
Injection of medicine with biological contamination into the patient
Risk:
The combination of probability of occurrence of patient harm by injection of medicine with biological contamination into the patient (hazardous situation)
and the severity of that harm
Harm
Illness (potentially severe) or even death​ of the patient
Damage to health caused by patient exposure to medicine with biological contamination
QRM TIP:
It is important to identify hazards to product quality that may ultimately lead to patient harm
The Hazardous Situation may lead to Harm
The Hazard leads to the Hazardous Situation

## Slide 12: How Hazards may be identified…
Hazard identification is the systematic use of information to identify potential sources of harm (hazards)
  Example: Information can include data from relevant studies, historical data, theoretical analysis, informed opinions, and the concern of stakeholders.
Hazard ID, as the first step of a risk assessment, begins with a well-defined problem description or “risk question”
  The "risk question" defines why the risk assessment is being performed and helps in defining the system and the appropriate scope of what will be studied
  It addresses the "What might go wrong?" question, including identifying the possible consequences of hazards
The output of the hazard identification step is the identification of the possibilities (i.e., hazards) that the risk event (e.g., impact to product quality) happens
What are the potential risks of introducing a second product to a single product facility?
What are the potential risks of changing sodium chloride suppliers for the ABC process?
Should this proposed change be approved? What risk mitigations would be required?
Examples of specific risk questions

## Slide 13: Hazards and their Potential Consequences Severity of harm
Patient Harm
What is the risk to patient safety of the identified hazard to product quality?
Product Quality Impact
What is the risk to manufacturing capability or product quality?
An appropriate severity scoring scale based on the risk question is important to define before initiating a QRM process. Consider the following examples of severity scales (for illustration only)
Severity | Definition
Critical | Life threatening illness or death
Major | Not life-threatening illness but hospitalization may be required
Moderate | Mild to moderate illness - doctor care may be needed
Marginal | Minor patient impact / minor illness
Negligible | No harm/inconvenience
Severity | Definition
Critical | Likely to lead to nonconforming and potentially harmful product. Products critical quality attributes not achieved
Major | Likely to lead to an in-process failure or deviation. However, potential exist for product to be released after investigation if critical quality attributes have been verified as achieved.
Moderate | Likely to push process conditions towards edge of failure, but still within specifications.
Marginal | Process may be impacted , but robust controls are in place to compensate and keep process within specifications.
Negligible | No process impact and no resultant product quality impact.
This severity scale describes the harm to patient safety
This severity scale describes the impact to manufacturing capability or product quality that may ultimately lead to patient harm

## Slide 14: QRM Tools for Hazard ID
There are well established QRM tools and methodologies available for hazard identification
Hazard Analysis and Critical Control Points
(HACCP)
Hazard and Operability Analysis (HAZOP)
Preliminary Hazard Analysis
Cause and Effect Diagrams (Ishikawa
Fishbone)
Process Mapping
and others…..
Different tools for hazard identification use different approaches that range from simply asking "What if" questions, to approaches that examine individual process steps (e.g., flow charts, process maps) or detailed drawings in a highly structured systematic way.
Examples of tools used for hazard identification are in the next slides.
Guidance on these methodologies is presented in ICH Q9(R1) – See Annex I.
See also the training material that is available in the ICH Q9 Briefing Pack on the ICH website.
QRM TIP
Many of the QRM tools listed on this slide identify hazards as well as include an analysis and evaluation of risks (i.e., the risk assessment).
This presentation focuses on Hazard ID and how to effectively use some QRM tools to complete the first step of the risk assessment.

## Slide 15: QRM Tools for Hazard ID Preliminary Hazard Analysis (PHA)
  Perform one hazard analysis per product
  Consider intended use and user populations
  Identify hazards to product quality that may ultimately lead to patient harm and that are related to manufacturing, testing, shipment, use, etc.
  Consider normal and fault conditions; consider normal use and foreseeable misuse
Document
Hazard Analysis
Purpose
Identify potential hazards, hazardous situations, and harm to patient (Note: a hazard may be associated with multiple harms)
Evaluate residual risk after mitigation
Quality Attribute / Product Requirement | Hazard | Sequence of Events | Hazardous Situation | Harm
Sterility | Biological contamination of the drug product | Drug product is contaminated during manufacture and patient injects into blood stream | Injection of bacteria or fungi | Potential for severe illness or death
Purity | Cross-contamination of one product with another product | Drug product is cross-contaminated during manufacturing with another product and patient takes the medicine | Unintended medicine administered to patient | Potential for severe illness or death
Identify the hazard
Identify the hazardous situation
A Preliminary Hazard Analysis is a QRM tool, and a version of it is shown below.
It demonstrates how hazards may be identified and documented.

## Slide 16
Methods
Machines
Materials
Measurement Systems
Environment
People
QRM Tools for Hazard ID
Cause and Effect Diagram (aka. Fishbone or Ishikawa Diagram)
The Fishbone Diagram is a simple technique that is commonly used to structure quality risk management activities, by organizing data and facilitating decision making.
It can be used to identify hazards, failure modes, root causes,​ and Corrective and Preventive Action (CAPA) focus areas.
The diagram is a visual way or a structured approach to look at the multiple underlying causes for an event or an effect and it can be used to identify potential sources of hazards.
For example, in a production process, a fishbone can used to look at the 6 main production areas: methods, machines, materials, measurement systems, environment, and people. Hazards identified in any of these areas can lead to hazardous situations and patient harm and need to be further evaluated.
Impact to product quality that can lead to patient harm
Hazards
Hazards
Hazards
Hazards
Hazards
Hazards
Note: See next slide for an example of an applied fishbone analysis
Fishbone Analysis is another useful tool for identifying hazards
Environment
People

## Slide 17: This is an example of how a fishbone analysis can be used for the introduction of new Isolator technology and aseptic filling to identify potential hazards
Hazard Identification
Risk Analysis
Risk Evaluation
CCIT = Container closure integrity test
CpK = Process capability
RH = Relative humidity
Fishbone Analysis Example
New isolator fill line (3) - Hazard ID
​
The first step for hazard identification is to ask well-defined questions for each of these areas, see some examples below
An Ishikawa diagram is used as a structured tool to identify the areas where hazards may appear
What hazards are possible in case of media fills?
What hazards are possible because of failure during vial sterilization?
What hazards are possible due to failures in product exposure time?
What hazards are possible when product not stored appropriately?
What hazards can occur in case of temperature modification?
Note: This slide is based on materials and figures submitted to the ICH Q9(R1) EWG by the Parenteral Drug Association (PDA).

## Slide 18
QRM Tools for Hazard ID Process Mapping (4)
Data & Process Mapping is another structured tool to visualize each step & connect the hardware, software, personnel, and documentation in each process, facilitating comprehensive data integrity hazard identification.
Hazard ID TIPs:
Seek the experiences of actual users and operators of the process or item under study
Ensure all aspects related to hardware, software, personnel & documentation (both paper and electronic) are considered
Nominate a moderator for the process mapping activity to ensure all voices are considered
Here is an example of data & process mapping of a hybrid login and set-up step of a manufacturing process.
The risk assessment team brainstorms about what can go wrong, and it focusses on human and technical hazards to data integrity.
Several human and technical data integrity hazards were identified at each process step (see red text boxes).
The data integrity hazards may have been missed had the team not used critical thinking and mapped the data and the process.
Data Integrity Hazard ID

## Slide 19: Creative Thinking & Teamwork in Hazard ID (5)
The probabilistic nature of risk can mean that risk assessment can be seen as quite an abstract activity for some. However, this can have a positive influence, especially when working to identify hazards, because it can lead to the use of imagination and creative thinking.
With the right mix of perspectives and experience, and when any subjectivity that arises is managed correctly, important hazards can be identified and their risks effectively managed.
When working to identify hazards, and when assessing the risks posed by them, it is important that different perspectives can be expressed and considered. Creative thinking within a multi-disciplinary team can facilitate this.
Multi-disciplinary teams are useful when performing hazard identification and risk assessments. This is because group collaboration supports creative thinking, problem solving, idea generation, discussing options, gaining alignment, and making decisions.
QRM Tip:
See the ICH Q9(R1) training material on Subjectivity in Quality Risk Management for information in relation to managing subjectivity.

## Slide 20
CASE STUDY
Hazard ID in New Product Development (6)
Step 1: Hazard Identification based on CQAs
The Critical Quality Attributes were identified as those product characteristics with a potential impact on patient safety, efficacy and product quality, based on a severity score, taking uncertainty considerations into account.
Using prior knowledge from similar products, structured brainstorming was carried out to identify potential hazards in relation to the new tablet product (based on the CQAs)
Using a Preliminary Hazard Analysis, the hazards and related product characteristics were ranked using the severity of harm associated with each hazard.
This case study, which concerns a tablet manufacturing process, describes a 2-step QRM approach, where an initial hazard identification that considers the Critical Quality Attributes (CQA) of the product is linked with a subsequent risk assessment of the various manufacturing unit operations. The ultimate goal was to define an appropriate control strategy to assure product quality and patient safety.
Note: This slide is based on materials and figures submitted to the ICH Q9(R1) EWG by the International Society for Pharmaceutical Engineering (ISPE).

## Slide 21
Risk Assessment based on Prior Knowledge to inform direction of experimental plan
CASE STUDY
Hazard ID in New Product Development
Step 2: Risk Assessment of the various manufacturing unit operations
The team then used prior knowledge to perform a risk assessment to identify which unit operations had the highest potential impact on the CQAs (and hence, potential for harm).
This allowed those unit operations to be subject to more detailed hazard identification from a manufacturing process perspective.
The unit operations with higher potential impact to product quality were given more focus in the experimental plan.
Throughout product development, experimental data were used to confirm the outputs of this initial risk assessment, which was based only on prior knowledge. This iterative process led to an appropriate control strategy and better risk-based decisions.
Note: This slide is based on materials and figures submitted to the ICH Q9(R1) EWG by the International Society for Pharmaceutical Engineering (ISPE).

## Slide 22
Hazards often have functional relationships with other hazards
  Interdependency between hazards should be taken into consideration
  Multiple hazards may combine to cause harm, rather than one hazard on its own
  Connecting the dots, we may find many hazards can lead to the same failure that may ultimately lead to patient harm
  Understanding this relationship is important to designing effective control strategies
Based on accumulated knowledge throughout the product lifecycle, risk review may identify new hazards that need to evaluated OR already identified hazards may need to be re-evaluated and may cause change to the control strategy
  Each CQA connects to hazards that define its manufacturing step control strategy
  As we gain new knowledge the control strategy may change over time
Maintenance throughout the product lifecycle (as an iterative process) can lead to adaptation/modification of the overall product control strategy (in line with ICH Q10 Pharmaceutical Quality System)
CASE STUDY
Additional Hazard ID Lifecycle Considerations
Hazards may be linked to other hazards
Risk review may identify new hazards
Control strategy adaptations
Note: This slide is based on materials and figures submitted to the ICH Q9(R1) EWG by the International Society for Pharmaceutical Engineering (ISPE).

## Slide 23: Key take-home points...
1. “Hazards” and “Risks” in the context of QRM are not equivalent and cannot be used interchangeably.
2. Hazard Identification, as part of QRM, is an essential first step that involves identifying what might go wrong (hazard).
3. The expectation is to identify hazards to product quality that may potentially lead to harm to the patient
4. There are different tools for hazard identification and selecting the right tool increases the effectiveness of the risk assessment
5. Hazard identification can be facilitated by lifecycle knowledge management and risk review activities.
* Note: Specific information in relation to the identification of Failure Modes is given in Part II of this presentation - ‘Considerations in relation to Failure Modes in the Pharmaceutical Environment’

## Slide 24: References
  ICH Q9(R1) - Quality Risk Management, January 2023
  Final Concept Paper: ICH Q9(R1) - Quality Risk Management, November 2020
  Based on material submitted to the ICH Q9(R1) EWG by the International Society For Pharmaceutical Engineering (ISPE), September 2021
  Baker, P, “Data & Process Mapping”, 26th Annual GMP by the Sea Conference, Cambridge, MD, USA, 2022
  Based on material and figures submitted to the ICH Q9(R1) EWG by Era Sciences Ltd., Ireland, September 2021
  Based on material and figures submitted to the ICH Q9(R1) EWG by the International Society for Pharmaceutical Engineering (ISPE), September 2021

## Slide 25: Further reading
  Vesper J., Risk Assessment and Risk Management in the Pharmaceutical Industry, Davis Healthcare International Publishing, 2006
  Quality assurance of pharmaceuticals. A compendium of guidelines and related materials. Volume 2, Second updated edition. Good manufacturing practices and inspection, WHO, 2007.
  Quality Improvement and Proactive Hazard Analysis Models: Deciphering a New Tower of Babel, National Academy of Sciences, 2004
  Application of Hazard Analysis and Critical Control Point (HACCP) methodology to pharmaceuticals, (Annex 7 to the report titled WHO Expert Committee on Specifications for Pharmaceutical Preparations), WHO Technical Report Series, No. 908, 2003, World Health Organization

## Slide 26: EWG Acknowledgment and Contact
Acknowledgement to ICH Q9(R1) Expert Working Group (EWG)
For any questions please contact the ICH Secretariat:
admin@ich.org