## Slide 1
Quality Risk Management, ICH Q9(R1)
Training Slides
Formality in Quality Risk Management
International Council for Harmonisation of Technical Requirements
for Pharmaceuticals for Human Use

## Slide 2: Legal Notice
This presentation is protected by copyright and may, with the exception of the ICH logo, be used, reproduced, incorporated into other works, adapted, modified, translated or distributed under a public license provided that ICH's copyright in the presentation is acknowledged at all times. In case of any adaption, modification or translation of the presentation, reasonable steps must be taken to clearly label, demarcate or otherwise identify that changes were made to or based on the original presentation. Any impression that the adaption, modification or translation of the original presentation is endorsed or sponsored by the ICH must be avoided.
The presentation is provided "as is" without warranty of any kind. In no event shall the ICH or the authors of the original presentation be liable for any claim, damages or other liability arising from the use of the presentation.
The above-mentioned permissions do not apply to content supplied by third parties. Therefore, for documents where the copyright vests in a third party, permission for reproduction must be obtained from this copyright holder.​

## Slide 3: Contents of this training material
The importance of formality in Quality Risk Management (QRM)
Background and guidance
The concept of formality in QRM
Three factors driving decisions on formality
  Uncertainty
  Importance
  Complexity
Examples of how decisions on formality in QRM can be made:
  QRM Process and Documentation
  QRM Tools
  Cross-functional Teams
  QRM Facilitators
Take-home Messages / Conclusions

## Slide 4
The Importance of Formality in QRM

## Slide 5: The Importance of Formality in QRM
Annex 1 in ICH Q9(R1) provides guidance on QRM Methods and Tools, and it include an overview of, and references to, some of the primary tools that might be used in QRM by industry and regulators. The Annex makes an important reference to Formality in QRM. It states the following:
  “It is neither always appropriate nor always necessary to use highly formal quality risk management methods and tools. The use of less formal quality risk management methods and tools can also be considered acceptable. See Chapter Section 5.1 for guidance on what constitutes formality in quality risk management.”
Chapter 5 of the Guideline, on QRM methodology, states that the degree of rigor and formality of QRM should reflect available knowledge and be commensurate with the level of uncertainty, importance and complexity of the issue to be addressed.
  That chapter deals not only with QRM tools, it also deals with Formality in QRM, Risk-based Decision-making and the need to manage and minimise the subjectivity that may impact every stage of the QRM process.
This training material addresses (1) what constitutes formality in QRM, (2) what different levels of formality might look like, and (3) how different levels of formality may be applied and documented.

## Slide 6: The Importance of Formality, cont’d
The second of these principles refers to formality, as shown above.
Formality in QRM is an important topic to understand, because the correct application of formality in QRM may lead to resources being used more efficiently, where lower risk issues are dealt with via less formal means, freeing up resources for managing higher risk issues and more complex problems that may require increased levels of rigour and effort.
Resource constraints should not be used to justify the use of lower levels of formality in the quality risk management process.
An understanding of formality can also support risk-based decision-making, where the level of formality that is applied may reflect the degree of importance of the decision, as well as the level of uncertainty and complexity which may be present.
The Guideline refers to two principles of QRM:
The evaluation of the risk to quality should be based on scientific knowledge and ultimately link to the protection of the patient. (Note: Risk to quality includes situations where product availability may be impacted, leading to potential patient harm.)
The level of effort, formality and documentation of the quality risk management process should be commensurate with the level of risk.

## Slide 7
The Concept of Formality

## Slide 8: A Spectrum of Formality
Applied formality
Formality is not a binary concept.
Rather, it is on a spectrum, with lower levels, higher levels, and levels in between.
It is considered a continuum.
Levels of formality at the lower part of the spectrum should be used for lower risk activities, in order to direct efforts appropriately to higher risk activities.

## Slide 9: What Formality in QRM looks like...
The following may be characteristics of higher levels of formality:
All parts of the quality risk management process (risk assessment, risk control, risk review and risk communication) are explicitly performed, and stand-alone quality risk management reports or related documents which address all aspects of the process may be generated and are documented (e.g., within the quality system).
Quality risk management tools, including those shown in Annex 1, are used in some or all parts of the process.
A cross-functional team is assembled for the quality risk management activity.
Use of a facilitator, with experience and knowledge of the quality risk management process, may be integral to a higher formality process.

## Slide 10: What Formality in QRM looks like...
The following may be characteristics of lower levels of formality:
One or more parts of the quality risk management process are not performed as standalone activities but are addressed within other elements of the quality system which may have risk assessment and risk control activities embedded within them.
Quality risk management tools might not be used in some or all parts of the process.
A cross-functional team might not be necessary.
Stand-alone quality risk management reports might not be generated. The outcome of the quality risk management process is usually documented in the relevant parts of the quality system.

## Slide 11
Note:
Degrees of formality between these higher and lower levels also exist and may be used.

## Slide 12: What Formality looks like...
Formality
QRM Process
QRM Tools used
Potential need for facilitation
Cross-functional team
Formality is expressed through a number of different factors.
These include the degree of uncertainty, complexity and importance that is associated with the QRM activity.
A consideration of these factors can help determine the appropriate degree of formality for the QRM task at hand.
The degree of formality that may be required is affected by these factors to different degrees, depending on the risk question.
The level of formality should be sufficient to allow for the robust management of risk.

## Slide 13
The factors driving the decisions about Formality in QRM

## Slide 14: Factors to consider in relation to Formality
Section 5.1 states that when determining how much formality to apply to a given QRM activity, these factors, among others, may be considered.
Uncertainty
Importance
Complexity
Each of these factors is explained on the following slides.
The ICH Q9(R1) guideline states that “in general, higher levels of uncertainty, importance or complexity require more formal quality risk management approaches to manage potential risks and to support effective risk-based decision making.”

## Slide 15: Uncertainty
Uncertainty:
The term ‘uncertainty’ in QRM means lack of knowledge about hazards, harms and associated risks.
The level of uncertainty that is associated with the area being risk assessed informs how much formality may be required to manage potential risks.
Systematic approaches for acquiring, analysing, storing and disseminating scientific information are essential for generating knowledge, which in turn informs all quality risk management activities.
Uncertainty may be reduced via effective knowledge management, which enables accumulated and new information (both internal and external) to be used to support risk-based decisions throughout the product lifecycle.

## Slide 16: Importance & Complexity
Importance:
The more important a risk-based decision may be in relation to product quality, the higher the level of formality that should be applied, and the greater the need to reduce the level of uncertainty associated with it (Ref. Section 5.1 of ICH Q9(R1)).
Complexity:
The more complex a process or subject area is to a quality risk management activity, the higher the level of formality that should be applied to assure product quality (Ref. Section 5.1 of ICH Q9(R1).

## Slide 17: Factors affecting Formality (Example )
Uncertainty
Importance
High
Low
Complexity
High
Low
High
Low
Cross- functional Team
Cross-functional team of SMEs assembled
Team assembled of several experts
Fewer SMEs are involved
QRM Tools Used
Quality Risk Management tools are used.
The use of tools may be limited
Quality Risk Management tools may not be needed
QRM Process
All steps of the QRM process are explicitly performed.
Some QRM steps are explicitly performed.
QRM is performed as part of routine activities within the PQS.
Potential Need for Facilitation
Use of experienced facilitator is integral
Facilitation may be beneficial
A facilitator may not be needed
.
Applied formality
High
Low
The above points may be characteristics of varying degrees of formality.

## Slide 18
Examples of how Decisions on Formality can be made

## Slide 19: QRM Process Considerations when Determining how much Formality to use
The QRM Process
All steps of the QRM process are explicitly performed.
Some QRM steps are explicitly performed.
QRM is performed as part of routine activities within the PQS
How important is risk question?
Risk Question
What is the level of uncertainty?
What is the complexity of the issue?
How extensive is the scope of QRM activity?
What is the impact and further use of the outputs of QRM?
Which parts of the QRM process should be explicitly performed?
This diagram is intended to visualise a thought process for deciding which parts of the QRM process need to be explicitly performed and how QRM activities should be documented.

## Slide 20: Other considerations...
How important is the risk question, and how important are the outputs of the QRM activity?
What is the level of uncertainty that is present? What kind of expertise and knowledge are required for the QRM activity and the risk question?
Is more than one group or department a stakeholder in the risk assessment or QRM activity? Is a cross-functional team needed?
How complex is the subject of the risk assessment or QRM activity, and would a QRM facilitator be advantageous?
Does a QRM tool need to be used?
  What would you need the tool to do to be able to answer the risk question?
  For example, is a quantitative assessment of risk required?
  Is a rigourous root cause analysis methodology required?
  How formal does the risk assessment need to be?

## Slide 21
Case Study 1 – Higher Level of QRM Formality
Building Assurance of Quality through Process Development
This case study demonstrates how a highly formal QRM process established a robust manufacturing platform.
Note: This case study is based on materials and figures submitted to the ICH Q9(R1) EWG by the International Society for Pharmaceutical Engineering (ISPE). Further information about this case study can be found in the ICH Q9(R1) training materials on Product Availability Risks.

## Slide 22
Process Development is an important and complex activity that necessitates rigorous studies to accomplish successful transfer to commercialization:
There can be variation in equipment, methods, raw materials, human factors and other elements that will ultimately determine process capability and performance
This variation can relate to:
  A lack of understanding of critical attributes of raw materials, and how they affect the physics and mechanics of processing.
  A lack of fundamental knowledge and understanding of scale-dependent factors.
  A lack of correspondence between equipment used in the lab and in the factory (e.g., where there are equipment and scale-up dependencies)
There can be a high degree of importance associated with process development and scale-up and getting to commercial manufacture.
Finite timelines and extreme pressures to market can curtail some of the process development activities.
Case Study 1: Highly formal QRM process
Uncertainty can be significantly reduced by increasing process understanding during the development stage and making quality-driven process design decisions.
Note: This slide is based on materials and figures submitted to the ICH Q9(R1) EWG by the International Society for Pharmaceutical Engineering (ISPE).
Notes: ​
​
​
​
​
​

## Slide 23
Robust conformance to CQAs are delivered through understanding the complex combination of raw material, formulation, and process variables.
As part of the Risk Assessment, the firm scored the impact of each unit operation on each CQA, as shown in the following table.
  Due to the high levels of uncertainty, importance and complexity, the firm engaged a cross-functional team and a QRM facilitator to ensure subjectivity in the Risk Assessment was minimized. The Risk Assessment team was in constant communication with management and had its endorsement for further studies to increase understanding.
The firm performed further iterative studies to increase process understanding and implemented needed risk controls to better ensure robust manufacturing reliability and consistent quality. This early focus on building strong process knowledge led to highly effective QRM decisions.
Case Study 1, cont’d
Building Better Design Knowledge
Note: This slide is based on materials and figures submitted to the ICH Q9(R1) EWG by the International Society for Pharmaceutical Engineering (ISPE).

## Slide 24
Initially, subject matter experts (SMEs) shared their opinions during early process development… this was based on prior knowledge.
Due to high levels of uncertainty, importance, and complexity, management engaged a cross-functional team and endorsed the use of a QRM facilitator.
Effective communication channels were established to ensure transparency between the QRM team and management.
Subsequently, process development studies provided iterative knowledge that improved both the accuracy of risk evaluations, and the effectiveness of risk controls.
Documentation of the various studies that were perforned facilitated effective Knowledge Management.
The management/risk review process monitored the effectiveness of established risk controls.
Management established a strategy and a threshold for re-visiting the initial risk assessment. This was based on inputs from the cross-functional team.
Case Study 1, cont’d
Summary
Note: This slide is based on materials and figures submitted to the ICH Q9(R1) EWG by the International Society for Pharmaceutical Engineering (ISPE).

## Slide 25
Case Study 2 – Lower Level of QRM Formality
Managing risks presented by a change to a tablet press
This case study demonstrates how a lower level of formality in QRM was applied as a part of the Change Control process

## Slide 26: Case Study 2: Lower formality QRM process
Case description – change to a tablet press
A tablet compression machine was designed, installed and validated for the manufacturing of tablets of product XYZ.
A risk assessment of the compression process was performed during process development.
This evaluated the robustness of the design of the tablet press.
Two years later, some components were at the end of their life and needed to be changed.
The new components were like-for-like to those in the original design, and the change control did not involve any change in the manufacturing process.
The importance of the change was evaluated as Moderate, because of the potential for production downtime during the change.
Knowledge of the risk scenarios related to the change of components was high, and so the level of uncertainty associated with the change control was Low.
How the components worked in the equipment design was well understood, and the complexity was regarded as Low.

## Slide 27
Uncertainty
Importance
High
Low
Complexity
High
Low
High
Low
Cross functional team
Cross-functional team of SMEs assembled
Team assembled of several experts
Fewer SMEs are involved
QRM Tools used
Quality Risk Management tools are used.
The use of tools may be limited
Quality Risk Management tools may not be needed
QRM Process
All steps of the QRM process are explicitly performed.
Some QRM steps are explicitly performed.
QRM is performed as part of routine activities within the PQS.
Potential need for facilitation
Use of experienced facilitator is integral
Facilitation may be beneficial
A facilitator may not be needed
.
Applied formality
High
Low
The above points may be characteristics of varying degrees of formality.
Case Study 2, cont’d
Factors affecting the degree of Formality

## Slide 28
Change acceptability was assessed inside change control system - no new risk assessment performed.
Deemed a minor change
The relevant SMEs assessed the change control.
All relevant knowledge of risk was already accessible.
No facilitator required
Rationale based on existing knowledge
Knowledge is leveraged from original risk assessments
No tool required
Case Study 2, cont’d
Factors affecting the degree of Formality

## Slide 29: Take-home Points/Conclusions
Regardless of how much formality is applied, the robust management of risk is the goal of the QRM process.
The use of higher levels of formality, lower levels of formality, and levels in between, can be appropriate depending on the situation.
The correct application of formality in QRM may lead to resources being used more efficiently; on the other hand, resource constraints should not be used to justify the use of lower levels of formality.
Formality in QRM is not a binary concept – it is best considered a continuum (or spectrum).
Three factors, Uncertainty, Importance and Complexity, are useful to consider when determining how much formality to apply to a QRM activity.
Formality is expressed through a number of practical characteristics:
  The extent of the QRM process that is applied,
  The use of a QRM facilitator,
  The involvement of a cross-functional team,
  The use of QRM tools.
An understanding of formality can support Risk-based Decision-making.

## Slide 30: Acknowledgment and Contact
Acknowledgement to ICH Q9(R1) Expert Working Group (EWG)
For any questions please contact the ICH Secretariat:
admin@ich.org